We assessed the code quality based on the specified requirements, and all criteria have been met:
- Comments make up at least 20% of the code.
- The duplication rate is below 5%.
- Each method and function contains fewer than 100 lines.
- There are always fewer than 7 levels of nesting.
- The cyclomatic complexity (McCabe's V(G)) is below 25.
- Tests cover at least 65% of the code.
Below are more details about each requirements and the methods we used to evaluate them.

- Comments has to represent at least 20 % of the code

- Duplication rate has to be inferior to 5%

Running the following command line to test the duplication rate, we obtain the results :

$  pylint --disable=all –enable=duplicate-code rastertools/

************* Module rastertools.cli.radioindice
rastertools/cli/radioindice.py:1:0: R0801: Similar lines in 2 files
==rastertools.cli.speed:[30:41]
==rastertools.cli.timeseries:[34:43]
        epilog="By default only first band is computed.")
    parser.add_argument(
        "inputs",
        nargs='+',
        help="Input files to process (e.g. Sentinel2 L2A MAJA from THEIA). "
        "You can provide a single file with extension \".lst\" (e.g. \"speed.lst\") "
        "that lists the input files to process (one input file per line in .lst)")
    cli.with_bands_arguments(parser)
    cli.with_outputdir_arguments(parser) (duplicate-code)
rastertools/cli/radioindice.py:1:0: R0801: Similar lines in 2 files
==rastertools.processing.sliding:[57:69]
==rastertools.radioindice:[476:488]
    with rasterio.Env(GDAL_VRT_ENABLE_PYTHON=True):
        with rasterio.open(input_image) as src:
        profile = src.profile

        # set block size
        blockxsize, blockysize = window_size
        if src.width < blockxsize:
        blockxsize = utils.highest_power_of_2(src.width)
        if src.height < blockysize:
        blockysize = utils.highest_power_of_2(src.height)

        # dtype and creation options of output data (duplicate-code)
rastertools/cli/radioindice.py:1:0: R0801: Similar lines in 2 files
==rastertools.cli.hillshade:[51:58]
==rastertools.cli.svf:[45:52]
        },
        "resolution": {
        "default": 0.5,
        "required": True,
        "type": float,
        "help": "Pixel resolution in meter"
        }, (duplicate-code)
rastertools/cli/radioindice.py:1:0: R0801: Similar lines in 2 files
==rastertools.cli.hillshade:[58:67]
==rastertools.cli.svf:[57:65]
    }
    for argument_name, argument_params in arguments.items():
        parser.add_argument(f"--{argument_name}", **argument_params)

    # add common arguments (inputs, output dir, window size, pad mode)
    parser.add_argument(
        "inputs",
        nargs='+', (duplicate-code)
rastertools/cli/radioindice.py:1:0: R0801: Similar lines in 2 files
==rastertools.cli.speed:[43:63]
==rastertools.cli.timeseries:[62:82]
    return rastertools_parsers

def create_speed(args) -> Speed:
    """Create and configure a new rastertool "Speed" according to argparse args

    Args:
        args: args extracted from command line

    Returns:
        :obj:`eolab.rastertools.Speed`: The configured rastertool to run
    """

    # get the bands to process
    if args.all_bands:
        bands = None
    else:
        bands = list(map(int, args.bands)) if args.bands else [1]

    # create the rastertool object (duplicate-code)

-----------------------------------
Your code has been rated at 9.98/10

The rate 9.98/10 suggests minimal duplication in the code, and therefore a duplication rate inferior to 5 %.

- Each method and function has to be inferior to 100 lines

Running the following command line to test the number of lines of functions and methods, we obtain the results :

$ pylint --disable=all --enable=too-many-statements rastertools

-------------------------------------------------------------------
Your code has been rated at 10.00/10 (previous run: 10.00/10, +0.00)

This command line tests if the number of statements in each method and function is inferior to 50. The rate 10,00/10 indicates that there is no function or method in the code that has more than 50 statements. Therefore, the requirement has been met.

- Imbrications has to be inferior to 7

Running the following command line to test the number of imbrications, we obtain the results :

$ pylint --disable=all --enable=too-many-nested-blocks rastertools/

--------------------------------------------------------------------
Your code has been rated at 10.00/10 (previous run: 10.00/10, +0.00)

This command line tests if the number imbrications is inferior to 5. The rate 10,00/10 indicates that there is no function or method in the code that has more than 5 nested loops. Therefore, the requirement has been met.

- Cyclomatic complexity McCabe V(g) has to be inferior to 25

Running the following command line to test the cyclomatic complexity, we obtain the results :

$ radon cc -s rastertools/

rastertools/rastertools.py
    M 90:4 Rastertool.process_files - A (4)
    M 53:4 Rastertool.vrt_dir - A (3)
    M 57:4 Rastertool.with_output - A (3)
    C 27:0 Rastertool - A (2)
    C 156:0 Windowable - A (2)
    C 20:0 RastertoolConfigurationException - A (1)
    M 36:4 Rastertool.__init__ - A (1)
    M 43:4 Rastertool.outputdir - A (1)
    M 48:4 Rastertool.keep_vrt - A (1)
    M 74:4 Rastertool.with_vrt_stored - A (1)
    M 117:4 Rastertool.process_file - A (1)
    M 134:4 Rastertool.postprocess_files - A (1)
    M 165:4 Windowable.window_size - A (1)
    M 170:4 Windowable.pad_mode - A (1)
    M 177:4 Windowable.with_windows - A (1)
rastertools/zonalstats.py
    M 387:4 Zonalstats.process_file - C (14)
    M 558:4 Zonalstats.__stats_to_geoms - C (14)
    M 493:4 Zonalstats.compute_stats - B (8)
    M 60:4 Zonalstats.__init__ - B (7)
    M 239:4 Zonalstats.__check_stats - B (6)
    M 344:4 Zonalstats.with_per_category - B (6)
    C 40:0 Zonalstats - A (3)
    M 122:4 Zonalstats.generated_stats_per_date - A (3)
    M 261:4 Zonalstats.with_output - A (3)
    M 303:4 Zonalstats.with_outliers - A (3)
    M 473:4 Zonalstats.postprocess_files - A (3)
    M 141:4 Zonalstats.generated_stats - A (1)
    M 146:4 Zonalstats.generated_stats_dates - A (1)
    M 151:4 Zonalstats.stats - A (1)
    M 156:4 Zonalstats.categorical - A (1)
    M 161:4 Zonalstats.valid_threshold - A (1)
    M 166:4 Zonalstats.area - A (1)
    M 171:4 Zonalstats.prefix - A (1)
    M 176:4 Zonalstats.bands - A (1)
    M 181:4 Zonalstats.output_format - A (1)
    M 186:4 Zonalstats.geometries - A (1)
    M 191:4 Zonalstats.within - A (1)
    M 197:4 Zonalstats.sigma - A (1)
    M 202:4 Zonalstats.chart_file - A (1)
    M 207:4 Zonalstats.geometry_index - A (1)
    M 212:4 Zonalstats.display_chart - A (1)
    M 217:4 Zonalstats.category_file - A (1)
    M 223:4 Zonalstats.category_file_type - A (1)
    M 228:4 Zonalstats.category_index - A (1)
    M 235:4 Zonalstats.category_labels - A (1)
    M 284:4 Zonalstats.with_geometries - A (1)
    M 324:4 Zonalstats.with_chart - A (1)
rastertools/hillshade.py
    M 96:4 Hillshade.process_file - C (11)
    C 25:0 Hillshade - A (3)
    M 52:4 Hillshade.__init__ - A (1)
    M 76:4 Hillshade.elevation - A (1)
    M 81:4 Hillshade.azimuth - A (1)
    M 86:4 Hillshade.resolution - A (1)
    M 91:4 Hillshade.radius - A (1)
rastertools/svf.py
    C 21:0 SVF - A (2)
    M 119:4 SVF.process_file - A (2)
    M 64:4 SVF.__init__ - A (1)
    M 85:4 SVF.radius - A (1)
    M 91:4 SVF.nb_directions - A (1)
    M 96:4 SVF.resolution - A (1)
    M 101:4 SVF.altitude - A (1)
    M 106:4 SVF.with_altitude - A (1)
rastertools/tiling.py
    M 105:4 Tiling.with_id_column - B (9)
    M 145:4 Tiling.process_file - A (5)
    C 24:0 Tiling - A (3)
    M 45:4 Tiling.__init__ - A (1)
    M 59:4 Tiling.grid - A (1)
    M 64:4 Tiling.output_basename - A (1)
    M 69:4 Tiling.output_subdir - A (1)
    M 74:4 Tiling.with_output - A (1)
rastertools/filtering.py
    C 22:0 Filtering - A (2)
    M 196:4 Filtering.process_file - A (2)
    M 138:4 Filtering.get_default_filters - A (1)
    M 150:4 Filtering.__init__ - A (1)
    M 172:4 Filtering.bands - A (1)
    M 177:4 Filtering.raster_filter - A (1)
    M 181:4 Filtering.with_filter_configuration - A (1)
rastertools/speed.py
    F 107:0 compute_speed - C (12)
    M 52:4 Speed.postprocess_files - B (9)
    C 27:0 Speed - A (5)
    M 35:4 Speed.__init__ - A (1)
    M 48:4 Speed.bands - A (1)
rastertools/main.py
    F 130:0 run_tool - B (9)
    F 248:0 _extract_files_from_list - A (3)
    F 30:0 add_custom_rastertypes - A (1)
    F 274:0 run - A (1)
rastertools/timeseries.py
    F 144:0 compute_timeseries - C (18)
    M 79:4 Timeseries.postprocess_files - C (11)
    F 235:0 _interpolate - A (3)
    C 31:0 Timeseries - A (3)
    M 36:4 Timeseries.__init__ - A (1)
    M 60:4 Timeseries.start_date - A (1)
    M 65:4 Timeseries.end_date - A (1)
    M 70:4 Timeseries.period - A (1)
    M 75:4 Timeseries.bands - A (1)
rastertools/utils.py
    F 34:0 to_path - A (4)
    F 62:0 get_metadata_name - A (3)
    F 89:0 slices_2d - A (3)
    F 15:0 to_tuple - A (2)
    F 45:0 get_basename - A (2)
    F 72:0 slices_1d - A (2)
    F 20:0 highest_power_of_2 - A (1)
    F 27:0 is_dir - A (1)
    F 56:0 get_suffixes - A (1)
rastertools/radioindice.py
    F 455:0 compute_indices - B (8)
    M 393:4 Radioindice.process_file - B (7)
    C 28:0 Radioindice - A (2)
    M 316:4 Radioindice.get_default_indices - A (1)
    M 332:4 Radioindice.__init__ - A (1)
    M 347:4 Radioindice.indices - A (1)
    M 352:4 Radioindice.merge - A (1)
    M 358:4 Radioindice.roi - A (1)
    M 362:4 Radioindice.with_output - A (1)
    M 379:4 Radioindice.with_roi - A (1)
rastertools/processing/algo.py
    F 707:0 _bresenham_line - B (8)
    F 634:0 svf - B (7)
    F 446:0 _local_sum - B (6)
    F 395:0 interpolated_timeseries - A (4)
    F 590:0 adaptive_gaussian - A (4)
    F 756:0 hillshade - A (4)
    F 507:0 median - A (2)
    F 558:0 local_mean - A (2)
    F 14:0 normalized_difference - A (1)
    F 36:0 tndvi - A (1)
    F 66:0 rvi - A (1)
    F 92:0 pvi - A (1)
    F 117:0 savi - A (1)
    F 142:0 tsavi - A (1)
    F 171:0 _wdvi - A (1)
    F 191:0 msavi - A (1)
    F 231:0 msavi2 - A (1)
    F 254:0 ipvi - A (1)
    F 280:0 evi - A (1)
    F 307:0 redness_index - A (1)
    F 328:0 brightness_index - A (1)
    F 349:0 brightness_index2 - A (1)
    F 370:0 speed - A (1)
    F 533:0 local_sum - A (1)
rastertools/processing/sliding.py
    F 26:0 compute_sliding - C (17)
    F 157:0 _read_dataset - A (5)
    F 120:0 _process_sliding - A (2)
    F 203:0 _sliding_windows - A (2)
rastertools/processing/vector.py
    F 43:0 filter - B (7)
    F 202:0 get_raster_shape - B (7)
    F 90:0 clip - B (6)
    F 246:0 rasterize - B (6)
    F 138:0 reproject - A (5)
    F 21:0 _get_geoms - A (3)
    F 173:0 dissolve - A (3)
    F 297:0 crop - A (3)
    F 336:0 vectorize - A (3)
    F 30:0 _get_geoms_crs - A (2)
    F 381:0 filter_dissolve - A (1)
rastertools/processing/stats.py
    F 66:0 compute_zonal_stats_per_category - C (15)
    F 274:0 _compute_stats - C (12)
    F 394:0 _gen_stats_cat - C (11)
    F 214:0 plot_stats - B (10)
    F 340:0 _gen_stats - B (10)
    F 25:0 compute_zonal_stats - A (4)
    F 168:0 extract_zonal_outliers - A (2)
rastertools/processing/rasterproc.py
    M 170:4 RasterProcessing.configure - A (3)
    M 180:4 RasterProcessing.compute - A (3)
    C 15:0 RasterProcessing - A (2)
    M 133:4 RasterProcessing.with_documentation - A (2)
    C 200:0 RadioindiceProcessing - A (2)
    C 233:0 RasterFilter - A (2)
    M 23:4 RasterProcessing.__init__ - A (1)
    M 68:4 RasterProcessing.__repr__ - A (1)
    M 72:4 RasterProcessing.name - A (1)
    M 77:4 RasterProcessing.algo - A (1)
    M 82:4 RasterProcessing.per_band_algo - A (1)
    M 88:4 RasterProcessing.nodata - A (1)
    M 93:4 RasterProcessing.dtype - A (1)
    M 98:4 RasterProcessing.in_dtype - A (1)
    M 103:4 RasterProcessing.compress - A (1)
    M 108:4 RasterProcessing.nbits - A (1)
    M 113:4 RasterProcessing.description - A (1)
    M 118:4 RasterProcessing.help - A (1)
    M 123:4 RasterProcessing.aliases - A (1)
    M 128:4 RasterProcessing.arguments - A (1)
    M 153:4 RasterProcessing.with_arguments - A (1)
    M 205:4 RadioindiceProcessing.__init__ - A (1)
    M 215:4 RadioindiceProcessing.channels - A (1)
    M 219:4 RadioindiceProcessing.with_channels - A (1)
    M 238:4 RasterFilter.__init__ - A (1)
rastertools/product/__init__.py
    F 21:0 s2_maja_mask - A (1)
rastertools/product/rastertype.py
    M 89:4 RasterType.add - C (14)
    M 339:4 RasterType.get_bands_regexp - B (7)
    M 251:4 RasterType.get_group - A (5)
    M 404:4 RasterType.get_mask_regexp - A (5)
    M 284:4 RasterType.has_channels - A (4)
    C 62:0 RasterType - A (3)
    M 75:4 RasterType.find - A (3)
    M 371:4 RasterType.get_mask - A (3)
    C 40:0 Band - A (2)
    M 44:4 Band.__init__ - A (2)
    M 70:4 RasterType.get - A (2)
    M 128:4 RasterType.__init__ - A (2)
    M 222:4 RasterType.accept - A (2)
    M 238:4 RasterType.get_date - A (2)
    M 299:4 RasterType.get_band_ids - A (2)
    M 307:4 RasterType.get_band_id - A (2)
    M 319:4 RasterType.get_band_descriptions - A (2)
    M 327:4 RasterType.get_band_description - A (2)
    M 388:4 RasterType.get_mask_ids - A (2)
    M 396:4 RasterType.get_mask_descriptions - A (2)
    C 20:0 BandChannel - A (1)
    M 48:4 Band.__repr__ - A (1)
    M 52:4 Band.identifier - A (1)
    M 57:4 Band.description - A (1)
    M 174:4 RasterType.__repr__ - A (1)
    M 178:4 RasterType.name - A (1)
    M 183:4 RasterType.product_pattern - A (1)
    M 188:4 RasterType.bands_pattern - A (1)
    M 193:4 RasterType.date_format - A (1)
    M 198:4 RasterType.maskfunc - A (1)
    M 203:4 RasterType.nodata - A (1)
    M 208:4 RasterType.masknodata - A (1)
    M 213:4 RasterType.channels - A (1)
    M 272:4 RasterType.has_channel - A (1)
    M 363:4 RasterType.has_mask - A (1)
rastertools/product/vrt.py
    F 18:0 _file2vrt - A (4)
    F 105:0 add_masks_to_vrt - A (4)
    F 143:0 set_band_descriptions - A (4)
    F 73:0 _func2vrt - A (2)
rastertools/product/rasterproduct.py
    F 529:0 _extract_bands_from_archive - C (11)
    M 288:4 RasterProduct.__get_bands - C (11)
    M 319:4 RasterProduct.__get_masks - C (11)
    F 583:0 _extract_bands_from_dir - B (9)
    M 213:4 RasterProduct.get_raster - B (9)
    M 54:4 RasterProduct.__init__ - B (6)
    M 356:4 RasterProduct.__create_vrt - B (6)
    C 32:0 RasterProduct - A (4)
    M 164:4 RasterProduct.get_date_string - A (4)
    M 185:4 RasterProduct.get_relative_orbit - A (3)
    F 493:0 _extract_bands - A (2)
    M 114:4 RasterProduct.free_in_memory_vrts - A (2)
    M 131:4 RasterProduct.channels - A (2)
    M 156:4 RasterProduct.get_date - A (2)
    M 176:4 RasterProduct.get_tile - A (2)
    M 197:4 RasterProduct.get_satellite - A (2)
    M 103:4 RasterProduct.__repr__ - A (1)
    M 106:4 RasterProduct.__enter__ - A (1)
    M 110:4 RasterProduct.__exit__ - A (1)
    M 121:4 RasterProduct.file - A (1)
    M 126:4 RasterProduct.rastertype - A (1)
    M 136:4 RasterProduct.bands_files - A (1)
    M 144:4 RasterProduct.masks_files - A (1)
    M 151:4 RasterProduct.is_archive - A (1)
    M 206:4 RasterProduct.open - A (1)
    M 418:4 RasterProduct.__wrap - A (1)
    M 444:4 RasterProduct.__apply_masks - A (1)
rastertools/cli/zonalstats.py
    F 148:0 create_zonalstats - A (5)
    F 10:0 create_argparser - A (1)
rastertools/cli/hillshade.py
    F 10:0 create_argparser - A (2)
    F 81:0 create_hillshade - A (1)
rastertools/cli/svf.py
    F 10:0 create_argparser - A (2)
    F 78:0 create_svf - A (2)
rastertools/cli/tiling.py
    F 10:0 create_argparser - A (1)
    F 85:0 create_tiling - A (1)
rastertools/cli/filtering.py
    F 68:0 create_filtering - A (4)
    F 10:0 create_argparser - A (3)
rastertools/cli/speed.py
    F 47:0 create_speed - A (3)
    F 10:0 create_argparser - A (1)
rastertools/cli/timeseries.py
    F 66:0 create_timeseries - A (5)
    F 12:0 create_argparser - A (1)
rastertools/cli/__init__.py
    F 7:0 with_window_arguments - A (2)
    F 37:0 with_outputdir_arguments - A (1)
    F 52:0 with_bands_arguments - A (1)
rastertools/cli/radioindice.py
    F 85:0 create_radioindice - C (12)
    F 12:0 create_argparser - A (3)

The maximum cyclomatic complexity McCabe V(g) obtained is 18, which is smaller than 25.

- Tests must cover at least 65% of the code

Running the following command line to compute the coverage of the tests, we obtain the results :

$ pytest --cov=~/pluto/rastertools/rastertools/ --cov-report=html

---------- coverage: platform linux, python 3.8.13-final-0 -----------
Name Stmts Miss Cover Missing
------------------------------------------------------------------------------
src/eolab/rastertools/__init__.py 15 0 100%
src/eolab/rastertools/cli/__init__.py 9 0 100%
src/eolab/rastertools/cli/filtering.py 25 0 100%
src/eolab/rastertools/cli/hillshade.py 17 0 100%
src/eolab/rastertools/cli/radioindice.py 46 0 100%
src/eolab/rastertools/cli/speed.py 16 0 100%
src/eolab/rastertools/cli/svf.py 19 0 100%
src/eolab/rastertools/cli/tiling.py 18 0 100%
src/eolab/rastertools/cli/timeseries.py 30 0 100%
src/eolab/rastertools/cli/zonalstats.py 39 0 100%
src/eolab/rastertools/filtering.py 43 0 100%
src/eolab/rastertools/hillshade.py 62 0 100%
src/eolab/rastertools/main.py 72 2 97% 281, 285
src/eolab/rastertools/processing/__init__.py 8 0 100%
src/eolab/rastertools/processing/algo.py 199 79 60% 421-442, 476, 525-530, 585, 610-631, 660-706, 785-823
src/eolab/rastertools/processing/rasterproc.py 85 5 94% 192-197
src/eolab/rastertools/processing/sliding.py 84 26 69% 80, 128-150, 181-200
src/eolab/rastertools/processing/stats.py 171 3 98% 104, 271, 317
src/eolab/rastertools/processing/vector.py 147 10 93% 37, 84-85, 196-197, 285-292
src/eolab/rastertools/product/__init__.py 9 0 100%
src/eolab/rastertools/product/rasterproduct.py 239 0 100%
src/eolab/rastertools/product/rastertype.py 168 1 99% 49
src/eolab/rastertools/product/vrt.py 69 3 96% 95-102
src/eolab/rastertools/radioindice.py 115 0 100%
src/eolab/rastertools/rastertools.py 54 0 100%
src/eolab/rastertools/speed.py 84 5 94% 133, 136, 138, 150, 152
src/eolab/rastertools/svf.py 42 0 100%
src/eolab/rastertools/tiling.py 72 0 100%
src/eolab/rastertools/timeseries.py 124 19 85% 180, 182, 184, 190, 192, 196, 198, 225, 244-256
src/eolab/rastertools/utils.py 42 0 100%
src/eolab/rastertools/zonalstats.py 243 0 100%
------------------------------------------------------------------------------
TOTAL 2366 153 94%

The tests cover 94% of the code, which is greater than the minimum requirement of 65%.